## Slide 1: IP Stacking (HA)
Jinqing Yan

## Slide 2: Background
Normally BFD with static routing mechanism is used in customer routers. BFD can be used to monitor the link state between Fee and external routers and router can do routing configuration dynamically.
However, that is not the all case. Some customers don’t use BFD but only static routing…which causes traffic lost if one or more Fees go down.

## Slide 3: What is HA
HA means traffic can always arrive to SBG when one or more FEE goes down and another FEEs can stack the lost external IP addresses (v4 and v6.

## Slide 4: More about HA
When node holding IP address changes, the ARP table on router should also be updated to new mac address.
To achieve this, one unsolicited ARP (Gratutious ARP) is sent out. https://wiki.wireshark.org/Gratuitous_ARP

## Slide 5: Cases related to stacking.
Node down (Fee down)
Both the configured IP addresses and stacked IP should be stacked on other Fees.
Fee Recover
Remove the ip addresses from stacking node.
Fee add
rebalance all fees’ loads ?
Fee remove (also node removed)
we need to stack the “stacked” IPs from this FEE to other Fees.

## Slide 6: How to detect external link down
Service unavailable detection.
If only controller crash, lwlbc can restore the services quickly.
If lwlbc crash or node down, tipc can detect the failure like “TIPC: factory DOWN for node 2, port id node 16781322 (ref 520123598)”, then service discovery can work .

## Slide 7: Fee Stacking ext IPs on eVIP
The automatic relocation and stacking of resilient FEE IP addresses is controlled by eVIP and can take place in response to failure detected by eVIP or can occur in response to recovery-related handling and system reconfiguration.
When starting the configurations.
When one fee node unavailable.
When fee node recover
Per ALB, the least "stacked" FEE (the one with the fewest external IP addresses assigned to it) is always chosen to host an IP. If there is a tie situation, the highest priority interface is chosen first. In order to stack on fixed nodes the configuration option for stacking fixed node must be set for each intended ALB.
The distribution of IP addresses on FEEs is checked periodically and will be rebalanced automatically as required

## Slide 8
node_unavailable_z / Evipc_util.c
For { each Fee in the “down” node }
fee_stacking_subnode_lost
Collect all stackable FEE nodes in the ALB and
sort by load in decreasing order and also by referring the floating priority.
For { each stacked IP in the “down” FEE }
> get the lowest load FEE (the last one in sorted list) as target node
> set the target node to current “down” FEE’s stacking host (stacking_host)
It indicates the “down” fee will be stacked on target FEE.
> add current stacked node in “down” FEE to the target FEE’s stacking list.
> update the stacked number on target FEE
> resort all stackable FEEs in the ALB in the decreasing order by load.
SEND_FEE_STACKING to all FEE
For { each FEE }
a. part_send_fee_stacking / parts.c
Here all external IPs in the stacked_list of one FEE are packaged and sent to this FEE.
b. set_stacked_address_request_h
this send the request to FEE and handled in protocol_h.c
active evipc detects one node unavailable

## Slide 9
FE controller handling with set_stacked_address_request_h
update_stacked_ips
Match all old stacked IP address against the requested IP address.
Remove IP from external interface, unmatched with request addresses.
Match requested IP address with old stacked IP address in FEE.
add new IP into external interface, unmatched with stacked IP addresses.
Send out GARP to update remote update ARP table.
Fee either add new ext. ip address into the external interface or remove old ip address from interface.

## Slide 10: IP Stacking in LWLB
Terms
IP Stacking on SC or LWLB
IPSS
Target Selection Rules
WB node down
WB node recover

## Slide 11: Terms
IP Stacking: a concept to stack “lost” ip addresses on some nodes.
Stackable Node: Node who is available take over the “lost” ip addresses.
Stacked Node: Node whose IP addresses are stacked on other nodes.
Unstacked Node: Node who needs to be stacked on other node.
Stacking Nodes: Nodes who are stacked on current Node.

## Slide 12: IP Stacking on SC or LWLB ?
Make stacking decision on SC
SC can see the whole cluster node. It make a simpler logical. However, SBG can use single SC and it takes 3-5 minutes to restore a SC service. That means traffic disturbance during these minutes if one or some TIPC or LWLBC node down.
Make stacking decision on LWLB Node.
each LWLB node should get the complete picture of the cluster. Current AdcWb can see the picture of services. So it needs a stacking FEE informations.
the disadvantage is LWLB need to save more cluster information. But it doesn’t impact traffics a lot.

## Slide 13: IPSS
IPSS, IP Stacking Scheduler, is node having the longest elapsed time in cluster.
responsible to figure out a stackable fee for the “lost” fee.
When a IPSS gone, the longest running node among the stackable nodes takes this role.
When a node gone, IPSS work out a node to stack the “lost” addresses and broadcast the result to cluster. The target node should stack the lost addresses when it receives the decision.
If the IPSS node gone during the working, new IPSS node should start new decision again.
If the target node is same as IPSS node, it should stack IP as soon as possible.
IPSS controls the synchronization of cluster stacking information

## Slide 14: Target Selection Rules
Rule:
stacked IPs of FEEs (Load) + ordered Fees’ Node by elapsed time.
Priority:
higher load, lower priority;
longer elapsed time, higher priority;
load is refered in advance of elapsed time when making priority.
Fee with highest priority should stack the “lost” external IP (v4 + v6);

## Slide 15: IP Stacking data synchronize when a node UP
Node A
IPSS
UP
Node available
IDEL
service announce
syncing
cluster stacking req
timeout
cluster stacking response
syned
Other node
.
.
.
.

## Slide 16
FEE Down Case
Add all to unstacked_fee_list
Sorted_stackable_fees_list
Remove node_a from sorted_stackable_fees_list
For each sorted_unstacked_fees {1…n}
Get_highest priority node from
sorted_stackable_fees_list
add node_a into unstacked_fee_list and resort sorted_unstacked_fees
node_a stacking addr
To stack on self
Broadcast target fee and
tobestacked fee information.
add ip to fee service;
Broadcast GARP packet.
Y
N
Y
N

## Slide 17
Stack tostacked address on my FEE.
Get tostacked fee information
Update target fee’s load ;
resort stackable fee;
Update stacked fee node to show where stacking current IPs;
The target node is me ?
Y
N
FEE Down Case

## Slide 18
FEE recover
Remove stacked IP from local FEE NS
FE bitmap in wb_a is set
(FEE service on Node_a available)
Update stacking FEE;
Update this old stacked FEE;
Update stackable FEE and resort;
If I stacked fee_a IPs
Y
N
The “lost” fee_a has already been stacked on node_b
Add fee to stackable list