## Slide 1: H248 Stream
Topology && RV && RG
Jinqing Yan
07/29/2016

## Slide 2
H248 Basic
Stream Topology
SDP for H248
RV and RG
Media Format Negotiation

## Slide 3: H248 Basic
Transaction
Descriptor
Action1 / ctx1
ActionN / ctxN
command

## Slide 4: H248 Basic
MediaDescriptor ::= SEQUENCE
{
termStateDescr TerminationStateDescriptor OPTIONAL,
streams CHOICE
{
oneStream StreamParms,
multiStream SEQUENCE OF StreamDescriptor
} OPTIONAL,
...
}
StreamDescriptor ::= SEQUENCE
{
streamID StreamID,
streamParms StreamParms
}
StreamParms ::= SEQUENCE
{
localControlDescriptor LocalControlDescriptor OPTIONAL,
localDescriptor LocalRemoteDescriptor OPTIONAL,
remoteDescriptor LocalRemoteDescriptor OPTIONAL,
...
}
LocalControlDescriptor ::= SEQUENCE
{
streamMode StreamMode OPTIONAL,
reserveValue BOOLEAN OPTIONAL, %% ON/OFF
reserveGroup BOOLEAN OPTIONAL, %% ON/OFF
propertyParms SEQUENCE OF PropertyParm,
...
}

## Slide 5: Stream Topology
ctx
audio SEP
ctx
LI mode
ctx
one-way mode
both-way mode
ctx
multi-streams
video SEP
SEP: stream endpoint

## Slide 6: Stream Topology
megaco/context
cmd1
cmd2
Call Controller
halfcall
halfcall
data path
control path / h248
network resource: bandwidth,QoS
DSP resource: transcoding, EC, NG

## Slide 7: SDP for H248
A single session description MUST NOT include more than one media description ("m=" line).
v=0
c=IN IP4 10.10.10.1
m=audio 1000 rtp/avp 0
m=video 62537 RTP/SAVPF 100
a=rtpmap:99 H264/90000
Stream=1 {
v=0
c=IN IP4 10.10.10.1
m=audio 1000 rtp/avp 0
},
Stream=2{
v=0
c=IN IP4 10.10.10.1
m=video 62537 RTP/SAVPF 100
a=rtpmap:99 H264/90000
}
Stream=1 {
v=0
c=IN IP4 10.10.10.1
m=audio 1000 rtp/avp 0
v=0
c=IN IP4 10.10.10.1
m=video 62537 RTP/SAVPF 100
a=rtpmap:99 H264/90000
}

## Slide 8: RV=ON && RG=ON
Reserve Resource Value
Reserve Resource Group
  v=0
  c=IN IP4 $
  m=audio $ RTP/AVP 0 8 18 100 110
  a=rtpmap:100 telephone-event/8000
  a=rtpmap:110 AMR/8000
  a=ptime:20
  v=0
  c=IN IP4 $
  m=image $ udptl t38
  a=T38UdpRedundancy
v=0
c=IN IP4 $
m=audio $ RTP/AVP 0 8 18 100 110
a=rtpmap:100 telephone-event/8000
a=rtpmap:110 AMR/8000

## Slide 9: Media Format Negotiation
!/2 [123.123.123.4]:55555 T = 10003 {
C = $ {A = ip/$/Ream1/$ {M {
ST = 1 {O {MO=SR, RV=ON, RG=ON},
L { v=0 c=IN IP4 $
m=audio $ RTP/AVP 0 8 18 100 110
a=rtpmap:100 telephone-event/8000
a=rtpmap:110 AMR/8000
a=ptime:20
v=0 o=- 0 0 IN IP4 192.168.1.35 s=-
c=IN IP4 $
m=image $ udptl t38
a=T38UdpRedundancy
},
R {v=0 c=IN IP4 192.168.1.35
m=audio $ RTP/AVP 0 100 18 110 120
a=rtpmap:110 telephone-event/8000
a=rtpmap:120 AMR/8000
a=rtpmap:100 PCMA/8000
a=ptime:20
v=0 c=IN IP4 192.168.1.35
m=image 2255 udptl t38
a=T38UdpRedundancy
}}},
ST=2{O{MO=SR, RV=OFF, RG=OFF},
L{ v=0 c=IN IP4 $
m=video $ RTP/SAVPF 99 120
a=rtpmap:99 H264/90000
a=fmtp:99 profile-level-id=4d0028;packetization-mode=1
a=rtpmap:120 VP8/90000
},
R{ v=0 c=IN IP4 10.10.10.5
m=video 62537 RTP/SAVPF 99 120
c= IN IP4 24.23.204.141
a=rtpmap:99 H264/90000
a=fmtp:99 profile-level-id=4d0028;packetization-mode=1
a=rtpmap:120 VP8/90000
}}},
A=ip/$/ream1/${M{
ST=1{……},
ST=2 {……}}}}

## Slide 10: Media Format Negotiation
!/2 [123.123.123.4]:55555 T = 10003 {
C = $ {A = ip/$/ream1/$ {M {
ST = 1 {O {MO=SR, RV=ON, RG=ON},
L { v=0 c=IN IP4 $
m=audio $ RTP/AVP 0 8 18 100 110
a=rtpmap:100 telephone-event/8000
a=rtpmap:110 AMR/8000
a=ptime:20
},
R {v=0 c=IN IP4 192.168.1.35
m=audio $ RTP/AVP 0 100 18 110 120
a=rtpmap:110 telephone-event/8000
a=rtpmap:120 AMR/8000
a=rtpmap:100 PCMA/8000
a=ptime:20
}}}}},
A=ip/$/ream1/${M{
ST=1{O {MO=SR, RV=ON, RG=ON},
L { v=0 c=IN IP4 $
m=audio $ RTP/AVP 0 8 18 100 110
a=rtpmap:100 telephone-event/8000
a=rtpmap:110 AMR-WB/16000
a=ptime:20
},
R {v=0 c=IN IP4 192.168.1.35
m=audio $ RTP/AVP 0 100 18 110 120
a=rtpmap:110 telephone-event/8000
a=rtpmap:120 AMR-WB/16000
a=rtpmap:100 PCMA/8000
a=ptime:20
}}}}}
dsp driver
codec list
dsp channel
audio/rtp
conf
pt value unmatch