## Slide 1: Traffic handling in eVIP
Incoming traffic
Jinqing Yan 2017/11/02

## Slide 2: Keywords
IPTABLES
IP ROUTING
FWMARK
HMARK
CONNTRACK
IPVS
ECMP
BFD
VRRP
OSPF
BRIDGE
VETH
MACVLAN

## Slide 3
FEE
FEE
SE
LBE
SE
LBE
Active
Standby
FEE
FEE
SE
LBE
SE
LBE
Active
Standby
ISER
/
CMX
SGC
/PL
SGC
/PL
SGC
/PL
SGC
/PL
ECMP
2 tuple hash {src ip , dst ip}
2 tuple hash
weighted round-robin
5 tuple hash
Basics (before is-sbg 5.9)

## Slide 4
FEE
SE
LBE
LBE
Active
Standby
FEE
SE
LBE
LBE
Active
Standby
ISER
/
CMX
SGC
/PL
SGC
/PL
SGC
/PL
SGC
/PL
ECMP
2 tuple hash {src ip , dst ip}
2 tuple hash
weighted round-robin
5 tuple hash
FEE runs on node has lower node id in a BS; SE runs on node has higher node id in BS.
On and after IS-SBG 5.9

## Slide 5: Basics
CMX
PL-1
PL-2
PL-3
PL-4
fee
fee
se
se
lbe
lbe
lbe
lbe
app
app
app
DPDK
app
DPDK
DPDK
DPDK
ECMP
{ fee:2, se: 2, lbe:4 }

## Slide 6: Incoming traffics handling before evip
SGC1
FEE
br0
mx00
mx25
bond0
bond0.116
veth
veth.116
evipdev
eth1.116
SE
LBE
SGC APP
ERS
SGCx
FEE
br0
mx00
mx25
bond0
bond0.116
veth
veth.116
evipdev
eth1.116
SE
LBE
SGC APP
ERS
OSPF/BFD
ISER
ECMP
ISER
ECMP
VRRP
BFD is standarded in RFC 5880

## Slide 7: Incoming traffics handling before evip
PL
FEE
br0
eth1
eth1.116
veth
veth.116
evipdev
eth1.116
SE
LBE
SGC APP
ERS
dpdk fw
KNI
lb
NS xx
llb interface

## Slide 8: Incoming traffics handling before evip (NATIVE)
ISER forwards incoming traffic to next hop based on ECMP
ECMP spreads incoming packets based hashing over source IP address and destination IP address.
It is expected that packets from same IP source always handled by same FEE;
It is not mandatory.
Traffics tagged with VLAN 116 are received on bond0.116 in name space vr_1.
blade_0_11:homer# ip netns exec vr_1 ip a show
    34: bond0.116@if7: <BROADCAST,MULTICAST,UP,LOWER_UP,M-DOWN> mtu 1500 qdisc noqueue master br0 state UP
    link/ether 04:4e:06:cf:31:59 brd ff:ff:ff:ff:ff:ff
    inet6 fe80::64e:6ff:fecf:3159/64 scope link
    valid_lft forever preferred_lft forever
    35: veth.116@if21: <BROADCAST,MULTICAST,UP,LOWER_UP,M-DOWN> mtu 1500 qdisc noqueue master br0 state UP
    link/ether e2:be:59:97:34:00 brd ff:ff:ff:ff:ff:ff
    inet6 fe80::e0be:59ff:fe97:3400/64 scope link
    valid_lft forever preferred_lft forever
    36: br0: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc noqueue state UP
    link/ether 04:4e:06:cf:31:59 brd ff:ff:ff:ff:ff:ff
    inet6 fe80::64e:6ff:fecf:3159/64 scope link
    valid_lft forever preferred_lft forever

## Slide 9: Incoming traffics handling before evip
iptables handle with these traffic as the front-end firewall
    blade_0_11:homer# ip netns exec vr_1 iptables -nvL -t raw | grep 10004
    0 0 ACCEPT udp -- * * 0.0.0.0/0 0.0.0.0/0 udp dpt:10004
    0 0 ACCEPT tcp -- * * 0.0.0.0/0 0.0.0.0/0 tcp dpt:10004
Bridge is used to link two interface as a switcher
    blade_0_11:homer# ip netns exec vr_1 brctl showmacs br0
    port no mac addr is local? ageing timer
    2 00:00:00:01:01:09 no 2.04
    1 00:00:00:01:01:0b no 2.04 // fee eth1.131 entry.
    2 00:13:5e:1f:39:d3 no 220.55
    2 04:4e:06:cf:31:59 yes 0.00 //where bond0.116 interface mapped.
    1 e2:be:59:97:34:00 yes 0.00
    LLB1fee_0_11:~# ip link show |grep "eth1.116\|00:00:00:01:01:0b"
    44: eth1.116@if20: <BROADCAST,MULTICAST,UP,LOWER_UP,M-DOWN> mtu 1500 qdisc noqueue state UP
    link/ether 00:00:00:01:01:0b brd ff:ff:ff:ff:ff:ff
veth Tech is used to forward packets from LLB namespace to default namespace
Now, the packet can arrive to FEE.

## Slide 10: Incoming traffics handling in FEE
FEE receives the packets and select a SE as next hop based on hashing over the src and dst IP address. The “hash value” modulo 256 is the “key” used to find the correct route table . So the FEE has 256 route tables, where each table points to a certain SE.
ERS
eth1.116
evip_macvlan0
IP handler
tunnel
route decision

## Slide 11
eth1.vlan
Pre-Routing Chain
routing match
Forward Chain
Post-Routing Chain
Tunnel Encapsulation
Routing Match for Tunneled Packets
Output Chain
Post-Routing Chain
evip_macvlan0
accepted
oif: Tunnel1 ;
forward
accepted
Match oif: Tunnel1 ;
Do HMARD/FWMARK
(2 tuple hash)
oif evip_macvlan0
accepted
accepted

## Slide 12
the packet firstly arrives to eth1.VLAN and is accepted by the PREROUTING chain.
Then, it matches the route rule and enter into the FORWARD chain and accepted.
    blade_0_5:~$ sudo ip netns exec LLB1-FEE_fe01_122 ip rule show
    5: from all to 10.21.0.4 lookup 4000001
    5: from 10.21.0.4 lookup main
    10: from all lookup local
    32766: from all lookup main
    32767: from all lookup default
    blade_0_5:~$ sudo ip netns exec LLB1-FEE_fe01_122 ip route show table 400001
    default dev Tunnel1 scope link
The handling continues and the PROROUTING chain makes a mark on this packet
    blade_0_5:~$ sudo ip netns exec LLB1-FEE_fe01_122 iptables -S -t mangle
    -A POSTROUTING -o Tunnel1 -g ALB0_SE
    -A ALB0_SE -j HMARK --hmark-src-prefix 32 --hmark-dst-prefix 32 --hmark-rnd 0xc175a3b8 --hmark-mod 256 --hmark-offset 3072
the HMARK marks the packet with a value ranging from 3072 to 3072+255. It makes a decision which route entry will be chosen to send packets out.

## Slide 13
3. Finally, the packet leaves POSROUTING chain and enters the IP TUNNEL handler.
4.Since the packet has already be marked in POSTROUTING chain. After encapsulated, it enters into the ip routing decision again and routes according to FWMARK.
5. The packets are accepted by OUTPUT chain and sent to interface driver.
blade_0_5:~$ sudo ip netns exec LLB1-FEE_fe01_122 ip -6 rule show from all fwmark 0xc00/0xffffff00 oif evip_macvlan0
blade_0_5:~$ sudo ip netns exec LLB1-FEE_fe01_122 ip -6 route show table all |grep evip_macvlan0
default via fe80::201:f5ff:fe01:125 dev evip_macvlan0 table 3072 metric 1024
default via fe80::201:f5ff:fe01:125 dev evip_macvlan0 table 3073 metric 1024
………………………..
default via fe80::201:f5ff:fe01:125 dev evip_macvlan0 table 3198 metric 1024
default via fe80::201:f5ff:fe01:125 dev evip_macvlan0 table 3199 metric 1024
default via fe80::201:f5ff:fe01:121 dev evip_macvlan0 table 3200 metric 1024
default via fe80::201:f5ff:fe01:121 dev evip_macvlan0 table 3201 metric 1024
…………………………………..
default via fe80::201:f5ff:fe01:121 dev evip_macvlan0 table 3325 metric 1024
default via fe80::201:f5ff:fe01:121 dev evip_macvlan0 table 3326 metric 1024

## Slide 14: Incoming traffics handling in LBE
LBE is designed based on IPVS. EVIP uses fwmark to represent a virtual server in IPVS. the available real servers are represented as internal IP address.
    blade_0_5:~$ sudo ip netns exec LLB1-LBE_fe01_120 ipvsadm -l
    IP Virtual Server version 1.2.1 (size=8388608)
    Prot LocalAddress:Port Scheduler Flags
    -> RemoteAddress:Port Forward Weight ActiveConn InActConn
    FWM 6000001 wrr persistent 178000
    -> 169.0.1.3:0 Route 10000 0 0
    -> 169.0.1.5:0 Route 10000 0 0
    FWM 6000002 IPv6 wrr persistent 178000
    -> [fc00::103]:0 Route 10000 0 0
    -> [fc00::105]:0 Route 10000 0 0
> The target pool in eVIP has all real server nodes.
  EVIP> show target-pools LLB1
  Target pools:
  VIP1 (id:1) (Sticky-group:yes) (Sched:wrr) (Udp-stateless:no) (All-undesignated:yes) PN 259 weight 100, PN 260 weight 100, PN 261 weight 100, PN 262 weight 100 )
  VIP2 (id:2) (Sticky-group:yes) (Sched:wrr) (Udp-stateless:no) (All-undesignated:yes) PN 259 weight 100, PN 260 weight 100, PN 261 weight 100, PN 262 weight 100 )

## Slide 15
Each flow policy in eVIP is given a unique fwmark, starting from 6000001. However ,flow policies towards same target pool configured with sticky_group=“yes” share same fwmark.
e.g. The flow policies towards target pool “VIP1” use same 6000001. flow policies towards target pool “VIP2” use 6000002.
EVIP> show flow-policies LLB1
Flowpolicies:
1e: VIP2_t10004 (0x974310)
3e: VIP2_u10004 (0x9a7650)
5e: VIP1_u10004 (0x96ff50)
7e: VIP1_t10004 (0x95f120)
21e: VIP2_u500 (0xa3bd00)
23f: VIP1_u500 (0x96bc40)
evip_macvlan0
conntrack
iptables
ip route
ipvs
tunnel

## Slide 16
evip_macvlan0
Pre-Routing Chain
routing match
INPUT Chain
Tunnel Encapsulation
Tunnel Decapsulation
Routing Matched
Output Chain
Post-Routing Chain
evip_macvlan0
accepted
Local Address
Local Deliver
mark
oif e_tun
accepted
accepted
IPVS Distribution
Routing Match for Real Server
Real Server Selected
OUTPUT Chian
Post-Routing Chiain
accepted
accepted

## Slide 17
1. the tunneled packet is received from SE over evip_macvlan0
  blade_0_5:~$ sudo ip netns exec LLB1-LBE_fe01_120 ifconfig evip_macvlan0
  evip_macv Link encap:Ethernet HWaddr 00:01:F4:01:01:20
  inet6 addr: fe80::201:f4ff:fe01:120/64 Scope:Link
  blade_0_5:~$ sudo ip netns exec LLB1-SE_fe01_121 ip -6 route show table all |grep evip | grep "table 2" | grep "fe80::201:f4ff:fe01:120" | wc -l
  128
Here we only have {2,2,2} topology for elements. So SE has 128 route entries for each LBE.
2. The tunneled packet is decapsulated to original packet in ipip_rcv() function.
3. The packet now enter into PREROUTING chain:
  blade_0_5:~$ sudo ip netns exec LLB1-LBE_fe01_120 iptables -S -t mangle | grep PREROUTING
  -P PREROUTING ACCEPT
  -A PREROUTING -j EVIP_HMARK_FORWARDING => relevant only for outgoing traffic
  -A PREROUTING -p icmp -m state --state INVALID -j EVIP_ICMP_INVALID
  -A PREROUTING -p icmp -m state --state INVALID -j DROP => safety check to avoid ICMP loops
  -A PREROUTING -j EVIP_CONNTRACK_FORWARDING => relevant only for replies to connections started from blades
  -A PREROUTING -p icmp -j EVIP_ICMP_CT_FWD => for incoming ICMP traffic
  -A PREROUTING -d 10.21.0.4/32 -p tcp -j EVIP_FP_VIP_ID_1_tcp => incoming tcp/udp/esp traffic for each VIP
  -A PREROUTING -d 10.21.0.4/32 -p udp -j EVIP_FP_VIP_ID_1_udp
  -A PREROUTING -d 10.21.0.4/32 -p esp -j EVIP_FP_VIP_ID_1_esp

## Slide 18
For the incoming traffic, the packet is marked with fwmark value ( from 6000001).
  blade_0_5:~$ sudo ip netns exec LLB1-LBE_fe01_120 iptables -S -t mangle | grep EVIP_FP_VIP_ID
  -A EVIP_FP_VIP_ID_1_esp -d 10.21.0.4/32 -p esp -j MARK --set-xmark 0x5b8d81/0xffffffff
  -A EVIP_FP_VIP_ID_1_tcp -d 10.21.0.4/32 -p tcp -m tcp --dport 10004 -j MARK --set-xmark 0x5b8d81/0xffffffff
  -A EVIP_FP_VIP_ID_1_udp -d 10.21.0.4/32 -p udp -m udp --dport 10004 -j MARK --set-xmark 0x5b8d81/0xffffffff
  -A EVIP_FP_VIP_ID_1_udp -d 10.21.0.4/32 -p udp -m udp --dport 500 -j MARK --set-xmark 0x5b8d81/0xffffffff
The mark is a input to IPVS and also the routing after leaving PREROUTING CHAIN.
4. The packet now enters into linux routing policy:
  blade_0_5:~$ sudo ip netns exec LLB1-LBE_fe01_120 ip rule show | grep 0x5b8d81
  100: from all fwmark 0x5b8d81 lookup 6000001
  blade_0_5:~$ sudo ip netns exec LLB1-LBE_fe01_120 ip route show table 6000001
  local default dev lo scope host
the above routing makes packet enter into ‘local’ handling and accepted by the ‘INPUT’ chain, except for a tcp packet is not known by the conntrack (state NEW).

## Slide 19
5. The packet is delivered to IPVS; IPVS matches the fwmark value and distribute (based on wrr) the packet to an available real server or a real server who is responsible for current connection.
  blade_0_5:~$ sudo ip netns exec LLB1-LBE_fe01_120 ipvsadm -l
  IP Virtual Server version 1.2.1 (size=8388608)
  Prot LocalAddress:Port Scheduler Flags
  -> RemoteAddress:Port Forward Weight ActiveConn InActConn
  FWM 6000001 wrr persistent 178000
  -> 169.0.1.3:0 Route 10000 0 0
  -> 169.0.1.5:0 Route 10000 0 0
Assume that the real server “169.0.1.3” (first pmp/bs) is selected here.
6. The packet now leaves IPVS and enter ROUTE again.
  blade_0_5:~$ sudo ip netns exec LLB1-LBE_fe01_120 ip rule show | grep "169.0.1.3"
  100: from all to 169.0.1.3 lookup 100259
  blade_0_5:~$ sudo ip netns exec LLB1-LBE_fe01_120 ip route show table 100259
  default dev e_tun_12 scope link
the route entries informs that the packet would be tunneled and sent out through e_tun_12.
The “OUTPUT” and “POST-ROUTING” chains accept the packet.

## Slide 20
8. The packet is encapsulated by tunnel and enters into routing again for tunneled ipv6 packet.
  blade_0_5:~$ sudo ip netns exec LLB1-LBE_fe01_120 ip route show table 100259
  default dev e_tun_12 scope link
  blade_0_5:~$ sudo ip netns exec LLB1-LBE_fe01_120 ip -6 tunnel show | grep e_tun_12
  e_tun_12: any/ipv6 remote fe80::200:ff:fe01:110 local fc00::200 dev evip_macvlan0 encaplimit 4 hoplimit 64 tclass 0x00 flowlabel 0x00000 (flowinfo 0x00000000)
  EVIP> show agents LLB1
  +---------------------------------------[ ALB LLB1 (ACTIVE) ]--------------------------------------+
  +----------------------------------------------- PN -----------------------------------------------+
  | pnagent (4) | lbesel_pn (22) |
  |[262] fe80::200:ff:fe01:114 : ACTIVE |[262] fe80::200:ff:fe01:114 : ACTIVE |
  |[261] fe80::200:ff:fe01:112 : ACTIVE |[261] fe80::200:ff:fe01:112 : ACTIVE |
  |[260] fe80::200:ff:fe01:110 : ACTIVE |[260] fe80::200:ff:fe01:110 : ACTIVE |
  |[259] fe80::200:ff:fe01:10e : ACTIVE |[259] fe80::200:ff:fe01:10e : ACTIVE |
  +--------------------------------------------------------------------------------------------------+
  | ersipc (0) | repdb (20) |
  |[262] fe80::200:ff:fe01:114 : ACTIVE |[262] fe80::200:ff:fe01:114 : ACTIVE |
  |[261] fe80::200:ff:fe01:112 : ACTIVE |[261] fe80::200:ff:fe01:112 : ACTIVE |
  |[260] fe80::200:ff:fe01:110 : ACTIVE |[260] fe80::200:ff:fe01:110 : ACTIVE |
  |[259] fe80::200:ff:fe01:10e : ACTIVE |[259] fe80::200:ff:fe01:10e : ACTIVE
9. Finally, the tunneled packet is sent out to PN through evip_macvlan0.

## Slide 21: Incoming traffics handling on PN
evip_macvlan0 receive packets from LBE. The received packet is a tunneled packet.
    blade_0_7:~$ ip -6 a show evip_macvlan0
    7: evip_macvlan0@eth3: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500
    inet6 fe80::200:ff:fe01:111/128 scope link
    valid_lft forever preferred_lft forever
    inet6 fe80::200:ff:fe01:110/128 scope link
    valid_lft forever preferred_lft forever
    inet6 fe80::201:4ff:fe01:103/128 scope link
    valid_lft forever preferred_lft forever
    inet6 fe80::200:ff:feff:104/64 scope link
2. The tunneled packet is accepted in “PREROUTING” chain and deliver to LOCAL since the destination is a local address.
3. The tunnel handler decode the packet’s ip header and gets the original packet.
4. The new packet enters into “PREROUTING” again and accepted. The routing match is trigger.
    blade_0_7:~$ sudo ip rule show |grep "10.21.0.4"
    5: from all to 10.21.0.4 lookup 2000003
    5: from 10.21.0.4 lookup 2000003
    blade_0_7:~$ sudo ip route show table 2000003
    default dev LLB1 scope link

## Slide 22
The packet now enters into ‘INPUT’ chain, where current FW is installed.
if all the rules pass, the packet finishes to go through IP stack and enters into TCP/UDP layer.
if the conntrack state is NEW, HMARK would calculate a mark value and iptables saves it into the CONNMARK.
    blade_0_7:~$ sudo iptables -S -t mangle
    -A INPUT -i LLB1 -m state --state NEW -g ALB0_sel
    -A ALB0_sel -j HMARK --hmark-src-prefix 32 --hmark-dst-prefix 32 --hmark-rnd 0xc175a3b8 --hmark-mod 256 --hmark-offset 2048
    -A ALB0_sel -j CONNMARK --save-mark --nfmask 0xffffffff --ctmask 0xffffffff
    -A ALB0_sel -j RETURN
The Layer4 put the payload data into TCP backlog queue and
wait for reassemble for segments, or the application reads
the TCP/UDP packets directly.
evip_macvlan0
Pre-Routing Chain
routing match
INPUT Chain
Tunnel Decapsulation
Layer-4 Handler
Application
accepted
Local Address
Local Deliver
Pass all FW rules
connmark