## Slide 1: Traffic before && on FEE
ospf, bfd, ecmp, bridge, namespace, iptables, ip route
2017/11/14

## Slide 2
FEE
FEE
SE
LBE
SE
LBE
Active
Standby
FEE
FEE
SE
LBE
SE
LBE
Active
Standby
ISER
/
CMX
SGC
/PL
SGC
/PL
SGC
/PL
SGC
/PL
ECMP
2 tuple hash {src ip , dst ip}
2 tuple hash
weighted round-robin
5 tuple hash
Load Balancer

## Slide 3: Incoming traffics handling before evip
SGC1
FEE
br0
mx00
mx25
bond0
bond0.116
veth
veth.116
evipdev
eth1.116
SE
LBE
SGC APP
ERS
SGCx
FEE
br0
mx00
mx25
bond0
bond0.116
veth
veth.116
evipdev
eth1.116
SE
LBE
SGC APP
ERS
ISER
OSPF/BFD
ECMP
NS-LLB

## Slide 4: Incoming traffics handling before evip
ISER forwards incoming traffic to next hop based on ECMP
ECMP spreads incoming packets based hashing over source IP address and destination IP address.
It is expected that packets from same IP source always handled by same FEE;
It is not mandatory.
Traffics tagged with VLAN 116 are received on bond0.1116 in name space vr_1.
blade_0_11:homer# ip netns exec vr_1 ip a show
    34: bond0.116@if7: <BROADCAST,MULTICAST,UP,LOWER_UP,M-DOWN> mtu 1500 qdisc noqueue master br0 state UP
    link/ether 04:4e:06:cf:31:59 brd ff:ff:ff:ff:ff:ff
    inet6 fe80::64e:6ff:fecf:3159/64 scope link
    valid_lft forever preferred_lft forever
    35: veth.116@if21: <BROADCAST,MULTICAST,UP,LOWER_UP,M-DOWN> mtu 1500 qdisc noqueue master br0 state UP
    link/ether e2:be:59:97:34:00 brd ff:ff:ff:ff:ff:ff
    inet6 fe80::e0be:59ff:fe97:3400/64 scope link
    valid_lft forever preferred_lft forever
    36: br0: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc noqueue state UP
    link/ether 04:4e:06:cf:31:59 brd ff:ff:ff:ff:ff:ff
    inet6 fe80::64e:6ff:fecf:3159/64 scope link
    valid_lft forever preferred_lft forever

## Slide 5: Incoming traffics handling before evip
iptables handle with these traffic as the front-end firewall
    blade_0_11:homer# ip netns exec vr_1 iptables -nvL -t raw | grep 10004
    0 0 ACCEPT udp -- * * 0.0.0.0/0 0.0.0.0/0 udp dpt:10004
    0 0 ACCEPT tcp -- * * 0.0.0.0/0 0.0.0.0/0 tcp dpt:10004
Bridge is used to link two interface as a switcher
    blade_0_11:homer# ip netns exec vr_1 brctl showmacs br0
    port no mac addr is local? ageing timer
    2 00:00:00:01:01:09 no 2.04
    1 00:00:00:01:01:0b no 2.04 // fee eth1.131 entry.
    2 00:13:5e:1f:39:d3 no 220.55
    2 04:4e:06:cf:31:59 yes 0.00 //where bond0.116 interface mapped.
    1 e2:be:59:97:34:00 yes 0.00
    LLB1fee_0_11:~# ip link show |grep "eth1.116\|00:00:00:01:01:0b"
    44: eth1.116@if20: <BROADCAST,MULTICAST,UP,LOWER_UP,M-DOWN> mtu 1500 qdisc noqueue state UP
    link/ether 00:00:00:01:01:0b brd ff:ff:ff:ff:ff:ff
veth Tech is used to forward packets from LLB namespace to default namespace
Now, the packet can arrive to FEE.

## Slide 6: Incoming traffics handling in FEE
FEE receives the packets and select a SE as next hop based on hashing over the src and dst IP address. The “hash value” modulo 256 is the “key” used to find the correct route table . So the FEE has 256 route tables, where each table points to a certain SE.
ERS
eth1.116
evip_macvlan0
IP handler
tunnel
route decision

## Slide 7: Incoming traffics handling in FEE
the packet firstly arrives to eth1.VLAN and is accepted by the PREROUTING chain.
Then, it matches the route rule and enter into the FORWARD chain and accepted.
    LLB1fee_0_11:~# ip rule show
    5: from all to 10.21.0.4 lookup 4000001
    5: from 10.21.0.4 lookup main
    10: from all lookup local
    32766: from all lookup main
    32767: from all lookup default
    LLB1fee_0_11:~# ip route show table 4000001
    default dev Tunnel1 scope link
The handling continues and the PROROUTING chain makes a mark on this packet
    LLB1fee_0_11:~# iptables -S -t mangle
    -A POSTROUTING -o Tunnel1 -g ALB0_SE
    -A ALB0_SE -j HMARK --hmark-src-prefix 32 --hmark-dst-prefix 32 --hmark-rnd 0xc175a3b8 --hmark-mod 256 --hmark-offset 3072

## Slide 8: Incoming traffics handling in FEE
the HMARK marks the packet with a value ranging from 3072 to 3072+255. It makes a decision which route entry will be chose to send packets out.
3. Finally, the packet leaves POSROUTING chain and enters the IP TUNNEL handler.
4. Since the packet has already be marked in POSTROUTING chain. After encapsulated, it enters into the ip routing decision again and routes according to FWMARK.
LLB1fee_0_11:~# ip -6 rule show
from all fwmark 0xc00/0xffffff00 oif evip_macvlan0
LLB1fee_0_15:~# ip -6 route show table all | grep evip_macvlan0
default via fe80::201:f5ff:fe01:106 dev evip_macvlan0 table 3072 metric 1024
………..
default via fe80::201:f5ff:fe01:106 dev evip_macvlan0 table 3327 metric 1024