## Slide 1: eVIP basic network
Jinqing Yan

## Slide 2: Agenda
eVIP Basic
Network Technology used in eVIP
Firewall in SBG Load Balance

## Slide 3: What is eVIP
eVIP (envolved VIP) is a Component Based Architecture (CBA) software-based system.
Applications in one cluster can share one external IP address, VIP addresses.
SBG Load Balance is implemented with eVIP.

## Slide 4: PCSCF Load Balancing
The VIP Load Balancing in the SBG allows the users on an access network to use one single IP address to access a set of SBG server blades that is configured in 1+1 redundancy pair.
The Load Balancer can serve 1 -15 Blade Pairs
The SBG Load Balancer is a Stateful L3 load balancer the distribution of traffic is based on the IP address of the UE.
Selection of SGC blade pair is performed when the first REGISTER message is received.
Network 1
SGC blade pair
SGC blade pair
SGC blade pair
Using VIP 1
IS Site
…
#15
#1
Load
Balancer

## Slide 5: Basic
Load
Balancer
SGC/PL
SGC/PL
SGC/PL
SGC/PL
ISER/CMX
ISER/CMX
1+1 redundancy
1+1 redundancy
Default Protocol:
ospfv2v3 for IS; static route on vSBG
ECMP used;
BFD used;
external

## Slide 6: Basic – Load Balancer
FEE
FEE
SE
LBE
SE
LBE
Active
Standby
FEE
FEE
SE
LBE
SE
LBE
Active
Standby
ISER
/
CMX
Signaling VLAN
I
P
v6 tunnels on internal VLAN in IS or eth3 on vSBG.
SGC
/PL
SGC
/PL
SGC
/PL
SGC
/PL

## Slide 7: Basic – Load Balancer
Front End Element (FEE): To attract traffic destined to the VIP address and forwards the traffic to a selected SE.
Security Element (SE): The SE element and IPsec function is optional in Load Balancer. In the SBG, the SE is configured not to be used. This still means that all packets, including ESP, are passing the SE element but not encrypted/decrypted
Load Balancer Element (LBE): Performs the load balancing based and forwards the traffic to the correct SGC in the correct blade pair.
Max number of LLB: 8
Max VIPs per LLB: 10
blade_0_15:~$ lxc-ls
llb1fee_0_15 llb1lbe_0_15 llb1se_0_15 llb2fee_0_15 llb2lbe_0_15 llb2se_0_15

## Slide 8: Basic – Element Selection
FEE
FEE
SE
LBE
SE
LBE
Active
Standby
FEE
FEE
SE
LBE
SE
LBE
Active
Standby
ISER
/
CMX
SGC
/PL
SGC
/PL
SGC
/PL
SGC
/PL
ECMP
round-robin
2 tuple hash {src ip , dst ip}
2 tuple hash
weighted round-robin

## Slide 9: Basic - Multiple VIPs in one LLB
LLB
VIP1-IPv4
VIP2-IPv4
VIP3-IPv4
VIP4-IPv6
VIP5-IPv6
Access Network 2
Access Network 1
Sign. Netw. Conn. IPv4
SIP Netw. Conn. v4 (VIP1-IPv4)
Sign. Netw. Conn. IPv6
SIP Netw. Conn. v6 (VIP4-IPv6)
SGC 1
Sign. Netw. Conn. IPv4
SIP Netw. Conn. v4 (VIP2-IPv4)
Sign. Netw. Conn. IPv4
SIP Netw. Conn. v4 (VIP3-IPv4)
Sign. Netw. Conn. IPv6
SIP Netw. Conn. v6 (VIP5-IPv6)
Access Network 3
Sign. Netw. Conn. IPv4
SIP Netw. Conn. v4 (VIP1-IPv4)
Sign. Netw. Conn. IPv6
SIP Netw. Conn. v6 (VIP4-IPv6)
SGC 2
Sign. Netw. Conn. IPv4
SIP Netw. Conn. v4 (VIP2-IPv4)
Sign. Netw. Conn. IPv4
SIP Netw. Conn. v4 (VIP3-IPv4)
Sign. Netw. Conn. IPv6
SIP Netw. Conn. v6 (VIP5-IPv6)
one LLB only
has one VR

## Slide 10: Basic - Configuration
IS MO
vSBG MO
IS GUI

## Slide 11
SGC
PCSCF
…
Parent child
Reference
Global MOC
AccessNetPcscf
networkId
networkName
vlanId
NextHopAddress
SipPa
vipAddressName
moRef: vipaddressRef?
ipAddress
tcpPort/udpPort
[0..998]
0..1
Interfaces
LoadBalancer
LLB
[0..8]
VIPAddress
ipAddress
Tcp/udpPort
sourceAddressStickiness
[0..10]
…
Blade System
[0..N]
1
Blade Systems
IntegratedSIte
1
Is SBG MO view
If you want two SIP Networks to use the same Load Balancer:
  Create two AccessNetPcscf/SipPa and let them use two different VIP addresses on the same LLB
If you want two Blade Pairs to handle traffic from one SIP network. :
  Create two AccessNetPcscf/SipP on the two Blade systems and and let them use the same VIP address
A vlan named “lb_internal_vlan” must be created firstly and reboot SGC to enable eVIP component.

## Slide 12: vSBG MO View
> eVIP component is always enabled in vSBG.

## Slide 13: GUI

## Slide 14: Basic – evipc CLI
Using “telenet fe80::1234%evip_macvlan0 25190” to login to eVIPc CLI.

## Slide 15: Basic – Code Modules
evipI.erl evipLoad.erl evipLib.erl evip.erl evipDtm.erl | evip_start.sh evip_startup_cmds.sh evip_get_vlan.sh evip_asilog.sh | evip_ch.upgSrc evip_gen.upgSrc evip_ch.appSrc evip_gen.appSrc
evip_dtm.c
evip component
telnet CLI
evip.xml

## Slide 16: Basic Technology in eVIP
Basic (vlan, route…)
VR (Linux namespace)
Veth/Bridge
Macvlan
IP6 Tunnel
Linux Virtual Server

## Slide 17
IP configuration for SIM ENV
By Ang Li

## Slide 18: VR
One LLB has one VR
the net id of access network who is the first one created to use this LLB is the VR of LLB.
eVIP uses default VR 0.
SGC / PL
router
bond0.116
/ eth1.116
VR 1
VR 0
llb
fee
se
lbe
SGC

## Slide 19: Veth/Bridge
veth – virtual ethernet can support the communication between two different namespace.
FEE
br0
eth1
eth1.116
veth
veth.116
evipdev
eth1.116
VR 1
VR 0
FEE
br0
mx00
mx25
bond0
bond0.116
veth
veth.116
evipdev
eth1.116
VR 1
VR 0
IS
SBGv
ip link add veth type veth peer name evipdev

## Slide 20: Macvlan
The internal communication with the LXCs eVIP uses macvlan. This makes the containers appear as another processor on the internal network.
ip link add link bond0.1119 evip_macvlan0 type macvlan mode bridge
FEE
evipdev
eth1.116
VR 0
FEE
evipdev
eth1.116
VR 0
IS
vSBG
bond0.1119
macvlan
SE
LBE
macvlan
macvlan
br
eth3
macvlan
SE
LBE
macvlan
macvlan
br

## Slide 21: Macvlan
blade_0_15:~$ cat /tmp/llb1fee_0_15.conf
lxc.utsname = llb1fee_0_15
lxc.network.type = macvlan
lxc.network.macvlan.mode = bridge
lxc.network.flags = up
lxc.network.link = bond0.1119
lxc.network.name = evip_macvlan0
lxc.network.hwaddr = 00:01:f6:01:01:08
lxc.network.type = vlan
lxc.network.vlan.id = 201
lxc.network.hwaddr = 00:00:00:01:01:09
lxc.network.name = eth1.201
lxc.network.flags = up
lxc.network.link = evipdev

## Slide 22: IP6 Tunnel
Traffics between two elements are over ipv6 tunnel.
It add an additional IP header to the raw packet.
It limits the MTU a packet from SGC or UE to 1480 B
FE
SE
LBE
PN

## Slide 23: IPVS
IPVS is used by LBE to distribute incoming traffic to a SGC application or forward a outgoing traffic to a SE element.
llb1lbe_0_11:~# ipvsadm -L
IP Virtual Server version 1.2.1 (size=8388608)
Prot LocalAddress:Port Scheduler Flags
-> RemoteAddress:Port Forward Weight ActiveConn InActConn
FWM 6000001 IPv6 wrr persistent 370000
-> [fc00::6e]:0 Route 6300 0 0
FWM 6000002 wrr persistent 370000
-> 169.0.0.110:0 Route 6300 0 0
LBE
e_tun_1
e_tun_2
e_tun_3
e_tun_4
LLB1lbe_0_11:~# ip route show table 100110
default dev e_tun_1 scope link
LLB1lbe_0_11:~# ip rule show
0: from all lookup local
100: from all fwmark 0xc00/0xffffff00 lookup 4112
100: from all to 169.0.0.110 lookup 100110

## Slide 24: Firewall
SGC / PL
router
bond0.116
/ eth1.116
VR 1
VR 0
llb
fee
se
lbe
SGC