## Slide 1: Load Balancer on vSBG
Node Detection
Jinqing Yan 2018/01/24

## Slide 2: Agenda
Basics
Floating Nodes
TIPC
Whiteboard

## Slide 3: Basics
CMX
PL-1
PL-2
PL-3
PL-4
fee
fee
se
se
lbe
lbe
lbe
lbe
app
app
app
DPDK
app
DPDK
DPDK
DPDK
ECMP
{ fee:2, se: 2, lbe:4 }

## Slide 4: Floating Nodes
The eVIP node is dynamically assigned to one of the undesignated
processing units that currently are available.
Each eVIP node is configured with a priority. Lower value has higher priority.
add node <nodeid> <hostname> OR floating <nodeid> <floatPriority>
    add node floating 1 1
    add node floating 2 1
    add node floating 3 3
    add node floating 4 4
nodeid > 256, floating node
nodeid <= 256, fixed node
The cmds are executed on first PMP

## Slide 5: Floating Nodes
Find the nodes information from evip CLI:
  EVIP> show hosts
  config id: 1 node id: 259 with hostname: 'blade_0_5'
  distribution: floating with priority 1.000000
  config id: 2 node id: 260 with hostname: 'blade_0_7'
  distribution: floating with priority 1.000000
  config id: 3 node id: 261 with hostname: 'blade_0_9'
  distribution: floating with priority 3.000000
  config id: 4 node id: 262 with hostname: 'blade_0_11'
  distribution: floating with priority 4.000000
Each config id is bond with a payload node id. The config id is what the “add node <nodeid> <priority>” add and the node id stands for a payload node.

## Slide 6: Node Detection
eVIP uses TIPC to detect a node’s status change.
1. When sbg invokes evip_start.sh, it extracts the last digit of ip address to make a TIPC address <zone.cluster.node>.
sudo tipc-config -netid=1234 -a=1.1.3 -be=eth:eth3
A tipc node only has one address, but can have one or more ports. Each port has unique port id <Z.C.N:ref> and port name <type, instance>

## Slide 7: Node Detection
2 sbg starts the evip factory service through evip_factory.sh. the factory reads the TIPC network address and generate a node id for current node.
#define WB_FLOATING_NODE_OFFSET 256
fs->node_id = WB_FLOATING_NODE_OFFSET | tipc_node(sa.addr.id.node);
Then we have the node id: 256 + 3 = 259.

## Slide 8: Node Detection
3 whiteboard is created on current node.
the factory service multicasts its available status to all nodes through tipc.
a factory sends the node information to evipc through protocol Z.
if (floating_node_id(wb_node_id)) {
assign_available_floating_node(f, node, wb_node_id);
add_floating_node_to_tps(f->evipc, NULL, wb_node_id);
if (evipc->state == EVIPC_STATE_ACTIVE) {
/* Get hostname of floating node */
get_node_hostname(f, wb_node_id);
}
}